## Slide 1: Chapter 9
Engine Cooling and Comfort Heating Systems/Diagnosis

## Slide 2
After studying Chapter 9, the reader will be able to:
Understand how the common automotive heating system works.
Explain what parts make up the heating system.
Understand how heater temperature is controlled.

## Slide 3: KEY TERMS
Bowden cable
Cellular
Control valve
Heater core
Hoses
Inlet hose
Outlet hose
Quick-connect coupling
Thermal cycling
Three-way design thermostat
Vacuum diaphragm or motor

## Slide 4: INTRODUCTION
As previously mentioned, the heating system resembles a small version of the engine’s cooling system.
  Some people consider the heater the most efficient part of the vehicle because it uses waste heat to warm the interior.
The heating system is made up of the heater core, hoses, and, in some systems, a control valve .

## Slide 5: Objectives (1 of 2)
Explain the engine cooling and comfort heating system and its major components.
Recognize the various components of the automotive cooling system.
Identify the different types of radiators.
Explain the operation and function of the coolant (water) pump.
Discuss the requirements for a closed cooling system.

## Slide 6: Objectives (2 of 2)
Explain the purpose and advantage and operation of a thermostat.
Recognize the safety hazards associated with cooling system service.
Explain the operation of various types of cooling fans.
Explain the need for a pressurized cooling system.
Explain the procedures for testing the various cooling system components.

## Slide 7: Engine Cooling System Components (1 of 3)
Engine closed cooling system
  Radiator and pressure caps
  Water pump, lines, and hoses
  Thermostat
  Coolant and coolant passages
  Pump drive devices

## Slide 8: Engine Cooling System Components (2 of 3)
Water pump moves coolant
Fan moves large volume of air
Radiator
  Heat to airflow
Pressure cap
  Raises boiling point of the coolant by pressurizing the system. 3 degrees per pound of pressure
  http://www.youtube.com/watch?v=DG-STqFiCg0
  http://www.youtube.com/watch?v=TlfzAKuDr8g

## Slide 9: Pressurized Cooling System
Maintained by cap
  Pressure is determined by the cap’s rating
  15-17 psi gasoline engine
  7 psi diesel
  Excess pressure is allowed to enter the recovery (overflow) tank
During cool down
  Vacuum created in the radiator
  Valve in the cap allows coolant to flow back from the recovery tank

## Slide 10: Engine Cooling System Components (3 of 3)
Coolant
  Water and antifreeze
Expansion tank (recovery tank)
Comfort heating system consists of all of the above plus:
  Heater core
  Water (coolant) control valve
  Heater hoses and/or lines

## Slide 11: Engine Cooling
Process by which heat is removed
Convection and conduction
35 percent of total engine heat is removed by the cooling system

## Slide 12: Cooling System
The engine cooling system removes excess heat and regulates the internal engine temperature to approximately 220°F.

## Slide 13: Radiator
Down or cross flow
Heat transfers from the coolant to the passing airflow
Copper, aluminum, and/or plastic

## Slide 14: Coolant Recovery System
Recovery/overflow tank
  Under atmospheric pressure
Expansion tank
  Sealed and pressurized with the pressure cap
Purges air from the cooling system
  May have a bleeder valve

## Slide 15: Engine Block and Cylinder Head Coolant Passages
Coolant water jackets
Expansion plugs
http://www.youtube.com/watch?v=mA9FemBpphw
http://www.youtube.com/watch?v=ouxbxE-BMNY

## Slide 16: Water (Coolant) Pump
Moves coolant through the system
Centrifugal type
  Enters at center, exits at edge
Draws coolant in through the lower radiator hose
Belt-driven
  External or timing belt
160-170 gpm at cruise
Contains a bypass passage
Water pump replacement precautions

## Slide 17: Auxiliary Water Pump Hybrid Electric Engine
In addition to an electric coolant circulation pump a large vacuum insulated coolant storage tank is incorporated.
Hot coolant can be stored for up to 3 days.

## Slide 18: Auxiliary Water Pump Hybrid Electric Engine

## Slide 19: Auxiliary Water Pump Hybrid Electric Engine

## Slide 20: Fan Shroud, Air Baffles, and Body Seals
Ram air effect
Purpose of fan shroud
Under vehicle air baffles

## Slide 21: Thermostat
Blocks coolant flow to the radiator until the engine is warm
  Wax pellets melt, causing the thermostat to open
Stuck open
  Engine runs below operating temperature; poor heater performance
  Overcooling
Stuck closed
  Engine overheats

## Slide 22: Thermostat
Temperature rating is marked on the thermostat
  This is the temperature at which it begins to open
  Fully open approximately 25°F later
  http://www.youtube.com/watch?v=T8cGKdICJmc

## Slide 23: Belt Drive Systems
Multi-rib and serpentine belts
Automatic adjustors
Belt tension
V belt

## Slide 24: Cooling Fans
Declutching Fan – Engine mounted
Flexible fans – Engine mounted

## Slide 25: Cooling Fans
Electric fans
  May come on even when the ignition switch is in the off position
  Control system and components
  May be one or two fan system

## Slide 26: Electric Cooling Fans
Basic electric radiator cooling fan wiring diagram
http://www.youtube.com/watch?v=iUuK5t-9fiQ

## Slide 27: Cooling Fans
To play, click the video screen.

## Slide 28: Cooling Fans
To play, click the video screen.

## Slide 29: Comfort Heating Systems
Heater core
  Heat exchanger is located in the passenger compartment duct system
  Comfort heating system
  Construction materials
    Plastic, aluminum, copper, brass

## Slide 30: Heater control valve
  Cable control
  Vacuum control
  Electronically controlled

## Slide 31: Comfort Heating Systems Hybrid Electric Engine
Positive Temperature Coefficient (PTC) heating element supplements heat produced from the heater core.

## Slide 32: Antifreeze (Coolant)
Ethylene glycol
  Standard ethylene glycol (green)
    two years, 36K miles
  Extended life (orange)
    five years, 100K – 150K miles
    Several types – OAT, HOAT, G-05, G-11, G-12, G-12 plus
  50/50 mixture offers best all-around protection
    Hydrometer
    Refractometer
Propylene glycol
  Low toxicity
  Can be used straight
Notes: Photo by Mark Schnubel

## Slide 33: Diagnosing Cooling System (2 of 3)
Inspect for visible indications of external or internal coolant leaks.
  Residue around hose connections or gasket surfaces
  Smoke from tailpipe
  Signs of leakage around expansion plugs

## Slide 34: Diagnosing Cooling System (3 of 3)
Pressure tests for internal and external leaks
  Connect the tester to the radiator cap.
  Apply pressure equal to the cap’s rating.
  Determine the point at which the cap pressure valve opened.
  Connect the tester to the radiator neck.
  Pressurize to the cap’s capacity.
  Observe the pressure and watch for external leaks.
    Pressure drop, no external leak – internal leak

## Slide 35: Diagnosing Cooling System (1 of 3)
Check the coolant level and condition and test for strength and acidity.
  May use a digital multimeter (DMM) to check acidity or poor ground condition.
    Both can cause serious cooling system and hose damage.
    Voltage reading should be below 0.10 volts DC

## Slide 36: Thermostat Operation
A thermostat should begin to open at its rated value.
If it begins to open more than +/-3°F from its rated value replace the thermostat.
The thermostat is generally fully open 25°F above its rated value.

## Slide 37: Belts and Tensioner
Inspect belt and tensioner condition
Check belt routing

## Slide 38: OPERATION
The inlet hose to the heater core connects to an outlet near the engine thermostat, or an area of the engine with the hottest coolant.
The outlet hose from the heater core runs to a connection near the inlet of the engine’s water pump, the area with the lowest coolant pressure.
  When the engine runs, coolant flows through the engine’s water jackets, past the thermostat, and through the heater core.
  The heated coolant warms the heater core and the air passing through it.

## Slide 39: OPERATION
ENGINE-OFF HEATER OPERATION
ELECTRIC AND HYBRID VEHICLE HEATING SYSTEMS

## Slide 40: HEATER CORE
The heater core is a heat exchanger much like the condenser, evaporator, and radiator.
  Heat transfers from the coolant, to the fins, and to the air passing through the core.
  As with other heat exchangers, there is a large area of fin-to-air contact to allow sufficient heat transfer and airflow.

## Slide 41: HOSES
Most heater hoses are made of reinforced rubber, which allows the flexibility needed to connect to a movable engine. SEE FIGURE 9–9 .
  Common hose sizes are 1/2, 5/8, and 3/4 inch (12.7, 15.8, and 19 mm).
  Some systems connect the hose to a metal tube that can be connected to the engine using either a threaded connector or a short hose section.
  This allows easier routing through congested or very hot areas around the engine that might cause hose failures.
RESTRICTORS

## Slide 42: CONTROL VALVES
Heater control valves can be ON-OFF or variable temperature control valves to adjust heater temperature.
  These valves are designed to modulate and adjust the flow so the core temperature can be controlled to all points between hot and cold.
  Some valves allow a return flow, so the coolant still circulates, bypassing the core when the valve is shut off.

## Slide 43: DUAL HEATING SYSTEMS
Larger vehicles with rear A/C systems include a heater in the rear unit.
  These rear units include a heater core and temperature-blend door. SEE FIGURE 9–12 .
The heater hoses include a tee fitting in each hose so heated coolant can flow through either or both heater cores.

## Slide 44: AFTERMARKET HEATING SYSTEM
Before heaters became standard equipment, aftermarket heating systems were installed in many cars.
  Today, these units are primarily designed for RVs, vans, and motor homes.
  They are normally installed after the vehicle has been built, by shops that specialize in heating and A/C service or RV van conversion and repair.
  SEE FIGURE 9–13 .

## Slide 45: SUMMARY
Hot coolant from the engine cooling system provides the heat for heater output.
Some vehicles have engine-off heater operation using an electric pump and control valves.
The heater core resembles a small radiator, and it is connected to the engine by a pair of hoses.
Some vehicles use a coolant flow valve to control heater output temperature.
Some vehicles use dual heater systems; these can be OEM or aftermarket.

## Slide 46: Overheating
http://www.youtube.com/watch?feature=endscreen&NR=1&v=hUzOTnsWImI